## Slide 1: Avoiding malicious nodes in wireless networks
9785-23-7
Notes: Change title to self-explanatory title (not technical)
Section presented by Daniel.

## Slide 2: Our Project Team
Daniel Davaris
Programming & Modelling
Curtis Richardson
System Operations & Documentation
Minjeong “Ellie” Kim
Research & Project Direction
Dr Yibe Alem
Project Sponsor
Maryam Sousani
Project Mentor
Notes: Detail responsibility sets at this slide

## Slide 3: Introduction
Our project tackles Black Hole nodes in mobile networks, which divert and block traffic. By employing Machine Learning, we aim to create a tool that detects and addresses this issue, improving network safety and efficiency. We apply a combination of academic and industry knowledge, employing structured planning and agile methods to safeguard networks and conserve energy.
Notes: Our project tackles Black Hole nodes in mobile networks, which divert and block traffic. By employing Machine Learning, we aim to create a tool that detects and addresses this issue, improving network safety and efficiency. We apply a combination of academic and industry knowledge, employing structured planning and agile methods to safeguard networks and conserve energy.

## Slide 4: Agenda
Introduction
What is the Benefit?
Project Parameters
Undertaking the Project
Key Lessons and Takeaways
Summary
3
5
14
17
22
27

## Slide 5: What is the Benefit?
Notes: What are the goals and value derived from project implementation
What is the benefit it is delivering?
Section presented by Curtis.
Less wasted communications with malicious neighbours
Less consumed energy via unnecessary communication with malicious neighbours

## Slide 6: Stakeholders
Smart Cars
Connected Farms
Smart Cities
Connected Infrastructure
Inter-space / inter-satellite comms
IoT Appliances and Applications
Notes: All stakeholders utilise AODV networks (generally, AODV is one of the implementable protocols available to each stakeholder)

## Slide 7: Areas of focus
Computationally Inexpensive
Low-powered devices
Often utilise own separate power supply (e.g. from battery)
Execution must be quick
Excellent Usability
Reasonable real detection and mitigation rates
Not reliant on proprietary technologies
Applicable to production networks
Notes: Computationally Inexpensive:
AODV-configured nodes generally low powered devices – CPU needs to be able to handle computational load
AODV-configures nodes often implemented as independent sensors, with its own separate power supply (from battery)
In cases where dangerous circumstances could arise (e.g. smart car collisions), the execution time of communication is extremely important
Excellent Usability:
Get real detection of malicious/Black Hole nodes to greater than 90%
Mitigation procedure
Develop drop-in model, able to be applied to current production networks

## Slide 8: Timeline
Follow-up review with Project Sponsor on Project Delivery
Jul 2023
Apply EOI for Project
Aug 2023
Create Project Plan
Sep 2023
Familiarisation with NS3
Oct 2023
Execute Machine Learning processes
Nov 2023
Create GitHub Project
Research AODV protocol and Black Hole Nodes
Customisation of NS3 files
Develop new Model
Deliver Project Presentation, Poster, and Report
Review previous group's Project documentation
Research Project implementation strategy similarity
Refinements to ML-based model against newly generated datasets
Attempt implementation

## Slide 9: Project Parameters
Notes: Scope / What the project is about
Section presented by Ellie.

## Slide 10
Effects of Black Hole Attack
Increase of packet loss
Reduced output of network
Increased delay
Denial of service
Notes: Black Hole node
Maybe 15 secs

## Slide 11: How can we capture and observe this behaviour?
?
?
Audience member

## Slide 12: Network Simulator Data Visualisation
Notes: Graphs (for presentation) of data output, go here (Data visualisation) - best to have gif or other full animation. To be input, once new model is created.
"Looks a little chaotic at first, but when broken down, it's fairly simple – just occurring in the span of microseconds."
Growing circles = broadcast message to find peers; saying "hello" to anything listening
"bullet" symbols travelling between nodes – packet payloads being sent to a destination peer (post neighbour discovery)
(spinning) square symbol falling from a node – dropped / aged off packet after Time To Live window has passed (or other limited parameter of the packet)

## Slide 13: Mobile Ad-hoc Networks
Singh Sengar, Sandeep & Singh, Alok & Narayan Tripathi, Pramod. (2011). A Survey on Telecommunication Technology Standards. Viewed 7 October 2023, <https://www.researchgate.net/figure/Architecture-of-MANET_fig1_241688995>
Decentralised Network
Reachable mobile within reception can be node
Nodes communicate neighbours for request of passing data
Limited bandwidth
Notes: A MANET is a type of wireless network where mobile devices communicate with each other directly without the need for a fixed infrastructure like routers or access points. Imagine a group of smartphones forming a network on the go, without relying on any central hub.
Description of MANETs – best to use a visual stimulus
Architecture of MANETs :
Singh Sengar, Sandeep & Singh, Alok & Narayan Tripathi, Pramod. (2011). A Survey on Telecommunication Technology Standards. Viewed 7 October 2023, <https://www.researchgate.net/figure/Architecture-of-MANET_fig1_241688995>
AODV flow chart will be here

## Slide 14: Ad-hoc On-demand Distance Vector Routing
Participating nodes forget neighbours
Routing table contains hop count number, address, sequence number, etc.
Nodes on route pass data packets and update their routing table
Notes: Description of AODV – best to use a visual stimulus
The flow chart on the screen shows the process of discovering the destination node through communication between source node and neighbour nodes.
*Hello message contains - the node's identification number - sequence number, - and list of neighbour nodes.
Routing table: hop count number
Routing table exists per communication attempt, and is then dropped. There is no persistent routing table (the neighbouring nodes must be mapped to a routing table each time the node needs to send a message).

## Slide 15
Black Hole Node
No direct communication between source node and destination node
Hop count and sequence number tend to be faked
High consumption of limited bandwidth
Notes: Ellie’s Flow Chart goes here (replaces table)
Black Hole node
Black hole node
Transcription for presentation:
Black hole node attack
A black hole node attack is a type of denial-of-service attack in which a malicious node in a network pretends to be a legitimate node and then drops any packets that it receives. This can cause a disruption in service for legitimate users of the network.
This flow chart shows how a black hole node advertises itself
A black hole node advertises itself as having the shortest path to all destinations by sending fake routing information to other nodes in the network. It can do this in a few ways:
Hello messages: Hello messages are used by nodes to announce their presence to other nodes in the network. A black hole node can include false routing information in its hello messages, such as claiming to have a route to all destinations with a hop count of 1.
Route request (RREQ) messages: RREQ messages are used by nodes to discover routes to destinations. A black hole node can send RREQ messages to other nodes in the network, claiming to have a route to all destinations.
Route reply (RREP) messages: RREP messages are used by nodes to reply to RREQ messages. A black hole node can reply to RREQ messages with fake routing information, claiming to have a route to all destinations.
Once a black hole node has advertised itself as having the shortest path to all destinations, other nodes in the network will start sending traffic to it. The black hole node will then drop all of the traffic that it receives.

## Slide 16: Network Simulator 3 Architecture
Software / Overall
Discrete Event Simulator
Modifiable simulation scenarios
User programs written in C++ or Python
Node
Computing device that connects to a network
C++ class "Node" provides methods for management and functions of computing devices in simulation
Application
Basic abstraction for program that generates some simulated activity
C++ class "Application" provides methods for simulation of activities
Channel
Simulated media via which data flows between nodes
C++ class "Channel" provides methods for simulating media types and behaviours
Net Device
Abstraction for simulated software drivers and hardware
C++ class "NetDevice" provides methods for simulated driver behaviours
Application
Node
Channel
Channel
Net Device
Net Device
Net Device
Channel
Net Device
Net Device
Net Device
Node
Node
Node
Application
Application
Application
Notes: Slide hidden, as too technical to be useful for capstone presentation (intended audience not familiar with NS3 and/or technical concepts).

## Slide 17: Network Simulator Data Vis.
Notes: Graphs (for presentation) of data output, go here (Data visualisation) - best to have gif or other full animation. To be input, once new model is created.

## Slide 18: Undertaking the Project
Notes: Section presented by Curtis.
What did we do
Challenges we had
What we have delivered
Changes we had along the way
Remember to say: We went to sponsor to discuss change and get it approved, when we noticed it wouldn’t be feasible
Use language of process “got it approved by sponsor”, etc.

## Slide 19: Challenges
Simulation Environment Setup
Trial and Error
Different base OSes and modules; git recursion
Patch availability
Project Goal Similarity
AODV/Black Hole mitigation originality
Focus on value desired goal can provide
Program Customisation
Understand NS architecture
Artefact handling and overall management
Generated datasets appropriate to execute ML against
Notes: Additional to challenge of undertaking technical research project, and also continue working on Project Management unit assessments
Simulation Environment Setup – getting the software to run/build, in the first place
Project Goal Similarity – ensuring our project provides value to wider academic and industry community; so much time spent getting other two aspects working, difficulties in staying focused on being able to discern the value we are aiming for
Program Customisation – NS3 is a very modular, and complex system: not only does the filesystem structure of the program need to be understood, but so too does the manner in which it outputs results (and how that can be customised through the different available modules – or even building your own modules)

## Slide 20: Changes
Jul 2023
Sep 2023
Oct 2023
Utilise NS2 for dataset generation
Use GitHub Project as source of truth for documentation (previously MS Teams)
Organise independent Azure instance during UC outage
Integrated graphical tool built-in
Notes: Remember to say: We went to sponsor to discuss change and get it approved, when we noticed it wouldn’t be feasible
Use language of process “got it approved by sponsor”, etc.

## Slide 21: Deliverables
Black Hole resistant model
Specifically, for AODV protocol based networks
Developed from dataset derived from simulated environment
Detection accuracy of model is 96%
Professional documentation
Target audience may desire sensor-based networks, but not understand the technical requirements
Mix of Project Management methodologies to suit needs
Enables iterative research

## Slide 22: So, was it a success?
?
?
Audience member
Notes: This is where we can pivot (with detail – obviously mention earlier in presentation if outcome was successful, or not)
A model has been developed, but it was not able to be implemented during the course of the capstone unit.
So close! Core components such as the detection model, educational documenation and materials, and a simulation environment capable of understanding Black Hole Nodes were all delivered. However, there wasn't enough time to implement the model into the that simulation environment.

## Slide 23: Key Lessons and Takeaways
Notes: Outcomes and recommendations; what did we learn
Section presented by Daniel.
Outcomes:
___
Learned:
1. Managing the process and flow of a highly academic research project
2. AODV protocol
3. Black Hole nodes and related malicious MITM attacks
4. NS3 software architecture and execution
5.
Recommendations:
___

## Slide 24: Education from Capstone
Networking
The AODV protocol
Vulnerabilities
Black Hole nodes and other related malicious MITM attacks for AODV
Machine Learning
NS2 & NS3 (tooling)
Software architecture and execution
Building environment, customising it to suit a particular use case, and getting useful output from simulations
Project Management
Managing the process and flow of a highly academic research project
Team Management
Time Management
Application of execution processes against moderately large datasets (1,000,000+ data points)
Notes: Learned:
1. Managing the process and flow of a highly academic research project
2. AODV protocol
3. Black Hole nodes and related malicious MITM attacks
4. NS3 software architecture and execution
5.

## Slide 25: Project Achievements
Detection model for Black Hole Nodes in AODV networks with accuracy of 96%
Reproducible Environment Build Instructions
Dataset generated through simulation environment, rather than fabricated data
Concise descriptions and documentation on AODV and Black Hole Nodes
Evidentiary documentation of conducting Project in professional manner
Notes: <Black Hole Node resistant modelling for AODV networks>
Reproducable Environment Build Instructions
Dataset generated through simulation environment, rather than fabricated data
Concise descriptions and documentation on AODV and Black Hole Nodes
Evidentiary documentation of conducting Project in professional manner <minutes, git merge process, gantt chart, etc.>

## Slide 26: Recommendations
Full utilisation of NS3 program
Refinements to energy usage modelling in NS3 program
Refinement of features exhibited by Black Hole Nodes
Higher complexity for Black Hole Node decision-making
Real-world network capture
Notes: Changes, depending on if we're recommending future groups' development, or our methods have succeeded

## Slide 27: Summary
Developed a machine learning model to confidently detect malicious nodes, though implementation was unsuccessful
Overcame various challenges:
  Configuration of network simulation software
  Data engineering for machine learning model training
Core project objective of detection model generation has been delivered
Notes: Section presented by Ellie.

## Slide 28: Thank you
9785-23-7
Curtis (u3201908) Daniel (u3215948) Ellie (u3225675)
Notes: “We’ll take questions, now.” (If no one wants to ask a question, pull some from our “back pocket”).
e.g.:
Q: "If this was the 2nd time this project was run, but it still wasn't 100% successful (implementation), how would you assist the university to have the confidence to attempt a 3rd time?
A: The major developments of the first attempt brought about significant feature engineering for the project; ours developed a robust direction for the project, as well as took the vast majority of the mystery out of dealing with the simulation environment (descriptions and documentation have been tightened up significantly, and requirements in order to utilise or customise the simulation environment have been clarified). While a future group will have some familiarisation with NS3 to contend with (and currency of research will always be a present issue), the project state is in a better place to allow more time to be spent on simulation and modelling experimentation.
“That brings us to the end of our presentation, thank you for your time.” – last line to be used.

## Slide 29: Bibliography
Singh Sengar, Sandeep & Singh, Alok & Narayan Tripathi, Pramod. (2011). A Survey on Telecommunication Technology Standards. Viewed 7 October 2023, <https://www.researchgate.net/figure/Architecture-of-MANET_fig1_241688995>
Notes: Bibliography slides